## Slide 1: Characterizing Honeybee Colony Dynamics Using Data Analytics: Preliminary Results
Kurt B. Ferreira, Ph.D
ABQBeeks Meeting
13 April 2023

## Slide 2: Who am I? Why am I Here?
Beekeeper since ~2018
~12 Hives in the Los Ranchos area
Hive styles: Langs, Layens and Top Bars
Researcher at Sandia National Labs
(Sometimes) Professor @ UNM in CS dept.
Research Area: Resilient Supercomputing Systems
(Acting) President, NMBKA
2nd Year NMBKA Cbeeks Student

## Slide 3: Goals
Characterize colony dynamics using hive sensor devices
Answer questions on:
  Winter honey consumption
  Strength of flow
  Forager field force size
  Robbing events
  Swarm prediction
Utilize standard “big data” analytics methods
Ultimate goal, open-source data from “sentinel hives” throughout the area for all beekeepers to utilize

## Slide 4: History of Hive Monitoring
Gates – 1914
  Monitored temperature and weight for a year
  Quantified winter honey consumption
  Demonstrated winter brooding though temperature tracking
Hambleton –1925
  Correlated ambient weather variables to hive weight
    Ambient temperature
    Relative humidity
    Hours of sunshine

## Slide 5: History of Hive Monitoring (cont’d)
Buchmann and Thoenes --1990
  Continuous weight monitoring
  Precision scale linked to a computer
  Recorded data every 15 min for 1 month
Meikle et al. -- 2006, 2008
  Recorded weight hourly over 16 months
  Showed the effects of swarming on daily detrended data
  Detected empty wooden hive daily weight change due to moisture changes in wooden hive bodies

## Slide 6: Hive Monitoring in the IoT Era
Numerous hobbyist devices
Monitor key hive metrics
  External/internal temperature and humidity
  Hive weight
  Entrance/Exit counters (gates and radar)
  Frequency/amplitude of colony members
  Vibration/Hive movement

## Slide 7: Hive Monitoring in the IoT Era (cont’d)
Cloud Storage
  Careful, many user agreements state you do not own your data!
Alert notification for urgent events
  Swarming/Absconding
  Queen loss
  Robbing
Problem: Analysis methodology questionable
  Methodologies not public or peer reviewed
  Lots of false positives
    Bi-weekly queen loss notification
    Dead/Swarm notifications
Remote
Monitoring

## Slide 8: Hive Monitoring Goals
Create analysis toolkit
  Process data using standard machine learning/data analytics techniques
  Classify critical events, correlating sensor data to observed conditions
  Compare against available vendor utilities, where possible
  Make data/analysis available to local beekeepers for analysis
Toolkit details
  Python: SciPy NumPy, pandas and matplotlib
  Code: https://github.com/NMBKA-Cbeeks/colony_trending.git
  Sensor Data (to appear): https://doi.org/10.5281/zenodo.7212455

## Slide 9: Hive Monitoring Questions?
Winter/dearth honey consumption – more accurate measure of honey needed
Flow strength – when to add/pull supers
Forager field force – how many bees are out flying?
Robbing
  Detection
  Rate of honey loss/gain
Swarming
  Detection
  Quantifying honey/bee losses

## Slide 10: Monitoring Hardware
Broodminder
  Scale under hive
  Temp/Humidity sensor – inside the hive
  14 frame Layens hive
  Carniolans
Bee Hive Monitoring, USA
  Scale under hive
  Hive Heart – temperature, humidity, frequency and audio recordings
  8-frame Langstroth hive
  Carniolans
Bee Hive Monitoring USA

## Slide 11: Hive Weight: Initial Analysis
7 months of weight data from a Layens-style hive
Two significant trends:
  Build-up
  Overwintering
Overwintering
Build-up

## Slide 12: “Detrending” Data
Two components in weight data
  Daily trend
  Trend over dataset
Daily trend
  Largely due to forager force departure and return and temperature changes
  Termed “seasonal trend”
  Use deconvolution methods to separate
Dataset trend
  Largely due to the colony drying, consuming and acquiring nectar as well bee birth and death
  Separate by generating a mathematical model

## Slide 13: “Detrended” Data
Assumptions:
  Assumes bee weights 0.11 grams
  Ignores drone weight (0.2 grams)
  Ignores diurnal weight changes due to water absorption/evaporation in wood or precipitation
  Does not account for bee death
Model changes to account for above, TBD

## Slide 14: Active Foragers
Field force peaks at ~15K bees
Possibility of undercounting foragers as drones weigh twice that of workers
Dips below still unexplained, likely due to assumptions

## Slide 15: Active Foragers Calculation – Temperature Compensation?
Claim: scale is temperature compensated
Expected: forager count is highly correlated with temp.
Unexpected: correlated with larger temperature ranges

## Slide 16: How much honey to leave for winter?
Use generated model to determine honey consumed
Use time outside growing interval for ABQ (~Oct 1 to present)
Conservative “carnie” colony, with significant top insulation.
0.07 lbs / day => 17 lbs
Interval Considered

## Slide 17: How much honey can bees collect from robbing?
Significant robbing event observed 10/04/2022 – 10/10/2022
Use simple polynomial regression
Acquisition during robbing event: 5.46lbs / day
Robbing event

## Slide 18: Ongoing Work
Complete year of data needed for statistically significant results
Additional colonies with different genetics
Additional hive styles and insulation.
Correlation with external metrics (precipitation, sunshine hours, internal/external temperature, etc.)
Correlation with other observation techniques (IR)
Comparison to vendor analytics
Open-source the data for comparison

## Slide 19: Summary
Modern IoT-based hive monitoring systems are growing in popularity
Current machine learning and data analytic methods have the potential to aid in understanding the volume of monitoring data
In this initial work, we showed the signal detrending can be used to determine a colonies foraging force, wintering consumption and robbing acquisition.
We also demonstrate some limitations in current systems/analysis (e.g. scales do not appear to be temperature compensated)

## Slide 20: Honey Consumption and Robbing Weight Changes
Consumption during confinement: -0.38 lbs / day
Acquisition during robbing event: 5.46lbs / day

## Slide 21: Hive Weight: Initial Analysis
Two+ weeks of weight data from Layens hive
Two significant events:
  Confined consumption rate: 9/23 – 9/27
  Robbing: 10/04 – 10/10
Robbing event
Confined due to weather

## Slide 22: Detrended Weight Data
Overall Trend
Daily Trend