## Slide 1: Characterizing Honeybee Colony Dynamics Using Data Analytics
Kurt B. Ferreira, Ph.D.

## Slide 2: Goals
Characterize dynamics using hive sensor devices
Answer questions on:
  Honey “burn” rate
  Strength of flow
  Forager field force
  Robbing
  Swarming
Utilize standard “big data” analytics methods
Ultimate goal, early warning system for urgent issues

## Slide 3: Hive Monitoring History
Gates – 1914
  Monitoring of temperature and weight for a year
  Quantified winter honey consumption weight
  Demonstrated winter brooding though temperature tracking
Hambleton –1925
  Correlated ambient weather variables to hive weight
    Ambient temperature
    Relative humidity
    Hours of sunshine

## Slide 4: Hive Monitoring History (cont’d)
Buchmann and Thoenes --1990
  Continuous weight monitoring
  Precision scale linked to a computer
  Record data every 15 min for 1 month
Meikle et al. -- 2006, 2008
  Recorded weight hourly over 16 months
  Showed the effects of swarming on daily detrended data
  Detected empty wooden hive daily weight change due to moisture content in wood

## Slide 5: Hive Monitoring in the IoT Era
Numerous hobbyist devices
Monitor key hive metrics
  External/internal temperature and humidity
  Hive weight
  Entrance/Exit counters
  Frequency/amplitude of colony members
  Vibration/Hive movement

## Slide 6: Hive Monitoring in the IoT Era (cont’d)
Clouds Storage
  Careful, many user agreements state you do not own your data!
Alert notification for urgent events
  Swarming/Absconding
  Queen loss
  Robbing
Analysis methodology questionable
  Methodology not public or peer reviewed
  Lots of false positives (bi-weekly queen loss notification)
Remote
Monitoring

## Slide 7: Hive Monitoring Goals
Analysis toolkit
  Process data using standard machine learning/data analytics techniques
  Classify critical events, correlating sensor data to observed conditions
  Compare against available vendor utilities, where possible
Toolkit details
  Python: SciPy NumPy, pandas and matplotlib
  Code: https://github.com/NMBKA-Cbeeks/colony_trending.git

## Slide 8: Hive Monitoring Questions?
Winter/dearth “burn” rate – more accurate measure of honey needed
Flow strength – when is add/pull supers
Forager field force – how many bees are flying?
Robbing
  Detection
  Rate of honey loss/gain
Swarming
  Detection
  Loss volume

## Slide 9: Monitoring Hardware
Broodminder
  Scale under hive
  Temp/Humidity sensor – inside the hive
  14 frame Layens hive
  Carniolans
Bee Hive Monitoring, USA
  Scale under hive
  Hive Heart – temperature, humidity, frequency and audio recordings
  8-frame Langstroth hive
  Carniolans
Bee Hive Monitoring USA

## Slide 10: Hive Weight: Initial Analysis
Two+ weeks of weight data from Layens hive
Two significant events occurred
  Robbing: 10/04 – 10/10
  Burn rate: 9/23 – 9/27
Robbing event
Confined due to weather

## Slide 11: “Detrending” Data
Two components
  Daily trend
  Trend over dataset
Daily trend
  Largely due to forager force departure and return
  Termed “seasonal trend”
  Use seasonal deconvolve methods to separate
Dataset trend
  Largely due to hive drying, consuming and acquiring nectar
  Separate by generating a mathematical model

## Slide 12: “Detrended” Data
Assumptions:
  Assumes bee weights 0.11 grams
  Ignores drone weight (0.2 grams)
  Ignores diurnal weight changes due to water absorption/evaporation in wood
  Does not account for bee death
  Model can be modified to account for above, TBD

## Slide 13: Active Foragers in Early fall
Field force peaks at ~8K bees
Possibility of undercounting foragers as drones weight twice that of workers
Dips still unexplained, may be due to iassumptions

## Slide 14: Quantifying Weight Changes
Two significant events occurred
  Confinement: 9/23 – 9/27
  Robbing: 10/04 – 10/10
Use simple polynomial regression for each interval separately.
Robbing event
Confined due to weather

## Slide 15: Honey ”Burn” Rate and Robbing Weight Changes
Consumption during confinement: -0.38 lbs / day
Acquisition during robbing event: 5.46lbs / day

## Slide 16: Ongoing Work?
Initial work, more data needed
Complete year of data needed for significant results
Additional colonies and separate genetics needed
Correlation with external metrics (precipitation, sunshine hours, etc.)
Comparison to monitor vendor analytics

## Slide 17: Summary
Modern IoT-based hive monitoring are growing in popularity
Current machine learning and data analytic methods have the potential to aid in understanding this vast monitoring data
In this initial work, we show how signal detrending can be used to determine a colonies foraging force.
We also show that robbing can increase weights by ~5.5 lbs per day and a confined fall-sized colony can consume ~0.5 lbs per day of honey.

## Slide 18: Detrended Weight Data
Overall Trend
Daily Trend